## Slide 1: ENTACT_505 – comparison
Sample from EPA ENTACT project
Overlap check:  align the results from MSS, msdial and xcms
  Rt_tolerance:0.2 min
  Mz_tolerance:0.015 Da
Major Parameters used:
  MSS: mz_error=10ppm, min_peak_width=5 scan, noise intensity threshold=2000
  Msdial:mz_error=10ppm, min_peak_width=10sec, noise intensity threshold =2000
  XCMS: mz_error=0.003Da(~10ppm by conversion), min_peak_width=7 scan, min peak height=2000
Feature numbers from the processed data:
  Msdial :21759
  Mss: 26242
  Xcms: 17257

## Slide 2: MSS vs XCMS
Reason: unique features mostly small peaks, the model built on the larger peaks

## Slide 3: MSS vs msdial

## Slide 4: Sample used
ENTACT sample from an EPA project
Multiple standards were spiked into samples, three samples were selected for the validation:
  ENTACT_505: 146 compound detected in instrument
  ENTACT_506: 150 detected
  ENTACT_507: 113 detected
All the detections were verified manually on raw data by checking the chromatograms

## Slide 5: Manual validation using ENTACT dataset
505 dataset
  Peak list generated 142 out of 147 matched, 5 didn’t match
  Peak picking function check 146 of 147 matched
  1 because scan number didn’t meet criteria
  4 because of mz slicing issue – didn’t select correct mz for peak picking
506 dataset
  Peak list generated 151 out of 153 matched, 2 didn’t match
  Peak picking function check 151 of 153 matched
  1 from pipeline because of mz slicing issue – didn’t select correct mz for peak picking, 1 has integration issue from mz slicing
  1 feature has been mis integrated
508 dataset
  Peak list generated 109 out of 113 matched, 1 unsure, 3 didn’t match
  Peak picking function check 111 of 113 matched
  2 because of bad peak shape/scan number
  2 because of mz slicing issue – didn’t select correct mz for peak picking
Chart: 
| Match | Unsure | Dismatch
Peak_list function | 402 | 1 | 10
Chart: 
| Match | Dismatch
Peak_pick manual check | 408 | 5

## Slide 6: Debugging
The integration and peak detection mismatch were mainly from mz slicing  proper mz were not selected thus detection was not completed
Current logic: slice the whole mz space by 2*err step
Refine: slice the whole mz space by 1*err step
Ideally: slice the whole mz space using density estimation