## Slide 1: Mass-suite: A novel open-source Python package designed for HRMS data analysis
Ximin Hu1, Derek Mar4, Nozomi Suzuki4, Bowei Zhang4, David A. Beck3, Edward P. Kolodziej2
1. Civil and Environmental Engineering, University of Washington, Tacoma, WA, United States. 2. Sciences and Mathematics (UWT); Civil and Environmental Engineering (UWS), University of Washington (Tacoma/Seattle), Tacoma, WA, United States. 3. Chemical Engineering, University of Washington, Seattle, WA, United States. 4. Materials Science and Engineering, University of Washington, Seattle, WA, United States.
Notes: Add logos

## Slide 2: Introduction
Why
Mass-suite
-Full-stack capability
-Python is popular
-Different angle of view
High Resolution Mass Spectrometry
-Novel technology
-Huge data
-Limited tools available
Environmental Pollutants
-Complicated in environment
-Challenge in identification & tracking
Notes: Novel tech – in env mostly used for water quality assessment,
Given its huge data collection capacity, it can help us understanding the pollutant behavior in water
There are lot of commercial or open-source packages, but rarely anyone providing a full-stack capability or overview angle of view for nta
Based on the most popular programming language python, mass-suite provides a full-stack capability of HRMS data processing and offering a unique angle of view for non-target analysis
More time emphasize mss
Python – Kaggle survey showed 81% users choose Python as primary programming language for data science related project, 2019

## Slide 3
Overview of Mass-suite
Always new
There are always something new:
Source identification
Source quantitative apportionment
MS2 data mining
Even more..
visualization
Various plot tools for visualizing HRMS data:
Chromatograms
Spectrums
Static/Interactive options
More..
Other tools
HRMS data processing assisting tools:
Formula annotation
MS2 spectrum online search
HRMS data quality report
More..
Data mining
Explore HRMS data with data science tools:
Principle Component Analysis
T-SNE Dimension reduction
Clustering analysis based on DBSCAN/OPTICS
Various modeling options
More..
data processing
Essential functions for HRMS data processing:
Mzml import
Peak picking & Alignment
Blank subtraction
Data curation
More..
Notes: Four major modules of Mass suite
Data processing covers basic needs such as peak picking, alignment, blank subtraction
Visualization tool includes interactive interface such as TIC, chromatogram and spectrum, and statistical summaries of the samples
The datamining tool is the core strength of the package, provides user better vision of their data
There are also other tools in the package assisting analysis, including..
Aside of those, new functions are keep updating

## Slide 4
Feature extraction & alignment
get_scans
peak_list
noise_removal
mss_align
Read mzml file into the pipeline
Extract peaks from chromatogram
Remove noise detections
Alignment of results from different samples
Python object
mz | rt | SN | score | peak area
300 | 10 | 100 | 1 | 1e7
… | … | … | … | …
mz | rt | SN | score | peak area
300 | 10 | 100 | 1 | 1.00E+07
… | … | … | … | …
mz | rt | SN | score | peak area
300 | 10 | 100 | 1 | 1.00E+07
… | … | … | … | …
mz | rt | SN | score | peak area
300 | 10 | 100 | 1 | 1e7
… | … | … | … | …
Avg. mz | Avg. rt | Avg. SN | Avg. Score | Sample 1 peak area | Sample 2 peak area | …
300 | 10 | 100 | 1 | 1e7 | 1e8 | …
… | … | … | … | … |  | …

## Slide 5
Feature extraction & alignment
get_scans
peak_list
noise_removal
mss_align
Read mzml file into the pipeline
Extract peaks from chromatogram
Remove noise detections
Alignment of results from different samples
mss_process
Avg. mz | Avg. rt | Avg. SN | Avg. Score | Sample 1 peak area | Sample 2 peak area | …
300 | 10 | 100 | 1 | 1e7 | 1e8 | …
… | … | … | … | … |  | …

## Slide 6
Example showcase
Data interactive interface
ms_chromatogram
Other options:
TIC plot
Isotopic plot
Peak Integration
ms_spectrum
Notes: Showcase 2

## Slide 7
Formula annotation
Interactive plot for HRMS data visualization
Feature annotation
With online/in-house database
…
Scan spectrum
Database spectrum
m/z
frag_comp
formula_prediction
Notes: Showcase 3

## Slide 8: Reliability
Comparison between different platforms
Annotation with in-house standards
Notes: As a new tool, the package needs to be reliable to users in order to produce robust results, thus two tests were conducted

## Slide 9
*Test done on the same sample (set of 3) with same parameter, XCMS processed on the web interface
XCMS
MSdial
Mass-suite
Mass-suite
XCMS
MSdial
Mass difference
Mass difference
RT difference
RT difference
Notes: Venn diagram showed majorities of features were overlapped from Mass-suite and selected platform, the distribution plot suggests the rt/mz slicing is comparable
Bigger texts for the plots

## Slide 10: Peak detection
Chart: 
| Match | Mismatch*
Peak_pick manual check | 408 | 5
* Mismatch derives from bad peak shape and function parameter settings
Samples with 413 known compound spiked were processed by Mass-suite
only matched through MS1 chromatograms using mz/rt pairs
Notes: Using a known compound spiked sample processed through mass-suite, the result showed 99% of the compound peaks in the list were found.

## Slide 11: Data mining
Statistical analysis
Clustering analysis
Quantitative source apportionment
Mass-suite provides various tools for Non-target HRMS data analysis

## Slide 12: Statistical analysis
PCA/T-SNE
Hypothesis
testing
Volcano plot
Similarity comparison
Etc.
Basic statistical analysis based on built-in python functions:
Notes: The statistical module provides essential analysis tools for common workflow

## Slide 13
Clustering analysis
Based mainly on Density-based spatial clustering of applications with noise algorithm
Cluster the features with similar trend
No need for detailed comprehension
Suitable for various studies
OPTICS algorithm as alternative
Chart: Time
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Trend1 | 1 | 0.7 | 0.5 | 0.3 | 0.1 | 0.07 | 0.05 | 0.03 | 0.01 | 0.007 | 0.005
Trend2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.7 | 0.5 | 0.3 | 0.1
Which one? | 1 | 0.6 | 0.6 | 0.3 | 0.15 | 0.12 | 0.05 | 0.05 | 0.01 | 0.005 | 0.005
Middle image source: https://scikit-learn.org/stable/auto_examples/cluster/plot_cluster_comparison.html#sphx-glr-auto-examples-cluster-plot-cluster-comparison-py
Notes: Clustering analysis provides a straight forward results of how the features look like when comparing to each others,
The algorithm aims at grouping the features that behaves similar while excluding the noises.
Advantage: showed as left, no need to know details for the data such as predefined cluster number, or data distribution; suitable for various studies such as time series, WWTP treatment assessment, or even spatial difference comparison

## Slide 14
  Distinguishing noise
  Find similar features with error tolerance
  Distinguish between different behaviors
* All data obtained from a time-series leaching experiment, normalization were conducted prior to clustering
Notes: Overall, the algorithm provides a quick and accurate approach for the feature prioritization

## Slide 15
Quantitative source apportionment
Modeling
Model options:
Linear regression
Lasso regression
Random Forest
SVM
…
Single chemical
Multiple clusters
Single cluster
Individual models
Ensemble method
Multivariate model
Single variate regression
Watershed mixtures*
* Reference: Katherine T. Peter et al., Application of Nontarget High Resolution Mass Spectrometry Data to Quantitative Source Apportionment, Environmental Science & Technology 2019 53 (21), 12257-12268 DOI: 10.1021/acs.est.9b04481
4% Highway runoff
Other Creeks
Creek A
Creek B
100% Highway runoff
30% Highway runoff
10% Highway runoff
?% Highway runoff
Notes: Using the sample on the left, combing with the clustering algorithm, here developed a modeling module in the package designated for the source quantitative analysis
There are flexible options, either using one chemical, multiple chemicals with similar behavior, or multiple groups chemicals with different trend, user can build their model and make prediction out of it

## Slide 16
Choose the option
Select among single chemical, single cluster or multiple clusters for modeling
feature_model
Built the model based on selected algorithm
cluster_pred
Get prediction of source apportionment using models
Quantitative source apportionment
Actual Conc.
Pred. Conc.

## Slide 17: Functionality Comparison
Tool Features | Mass-suite | TidyMS | MZmine2 | XCMS* | MS-DIAL
Language | Python | Python | Java | R | C#
Rawdata preprocessing | √ | √ | √ | √ | √
QC-based batch correction | × | √ | × | × | ×
Quality reports | √ | √ | √ | × | √
Normalization, imputation, scaling | √ | √ | √ | × | √
Feature annotation | √ | × | √ | × | √
Isotope grouping | × | × | √ | √ | √
Interactive visualization plots | √ | × | √ | × | √
Clustering statistical analysis | √ | × | × | × | ×
Modeling tools | √ | × | × | × | ×
* XCMS is supported by various of R packages and mostly functioning as a starting point
** Functionality counted could be missing some features due to delay of software update
Reference: Riquelme G, Zabalegui N, Marchi P, Jones CM, Monge ME. A Python-Based Pipeline for Preprocessing LC-MS Data for Untargeted Metabolomics Workflows. Metabolites. 2020 Oct 16;10(10):416. doi: 10.3390/metabo10100416. PMID: 33081373; PMCID: PMC7602939.
Notes: Here is a comparison chart, As mentioned at beginning ,mass-suite is designed towards full-stack capacity, and it built it’s novelty on the datamining tools especially the clustering analysis
Formatting to hightlight

## Slide 18
70%
Agreement on feature detection
As reliable as other platforms
99%
Accuracy of peak picking
With additional scoring based on RandomForest model
8 min/file*
Average processing time
Capable to be boosted up by supercomputers
*Tested under default parameters as intensity cutoff = 3000, mz error = 10 ppm, alignment mz error = 10 ppm, rt error = 0.5 min, model_scoring was off, test were performed on personal laptop (Intel(R) Core(TM) i7-7700HQ CPU, 16GB RAM)
4 Tools
Powering Non-target analysis
Based on data science approaches
30 Mb
Package size
Light for the installation and use
Open Source
Of the entire package
Keep updating, anyone can be involved
Benchmarks
Notes: Statistical tools, clustering tools, modeling tools and source identification tool (in dev)
Here are some benchmarks for the tool, As shown above, the tool is reliable, portable, and flexible

## Slide 19: Development Roadmap
1
3
5
6
4
2
Annotation tool
Testing
Dynamically update
Source identification
GUI/web tool
Even more…
Notes: Here is a roadmap for future development, will start from public beta test/debugging, finish up some tools such as annotation, identification and non-programmer friendly interface
The package will keep updating according to the feedback and needs

## Slide 20: Related information
Installation:
  https://pypi.org/project/mass-suite/
Github page & documentation:
  https://github.com/XiminHu/mass-suite
Contact:
xhu66@uw.edu
Suggestions & Collaborations
are always welcome !

## Slide 21
Acknowledgement:
  A big shout to Professor Edward Kolodziej, Professor David Beck, Dr. Katherine Peter, and the Center for Urban Waters for all their help during the development of this package.

## Slide 22: References & dependencies
M Kösters et al; pymzML v2.0: introducing a highly compressed and seekable gzip format, Bioinformatics, doi: https://doi.org/10.1093/bioinformatics/bty046
Pedregosa et al., Scikit-learn: Machine Learning in Python, JMLR 12, pp. 2825-2830, 2011.
Martin Ester et al. 1996. A density-based algorithm for discovering clusters in large spatial databases with noise. In Proceedings of the Second International Conference on Knowledge Discovery and Data Mining (KDD'96). AAAI Press, 226–231.
Riquelme G et al. A Python-Based Pipeline for Preprocessing LC-MS Data for Untargeted Metabolomics Workflows. Metabolites. 2020 Oct 16;10(10):416. doi: 10.3390/metabo10100416. PMID: 33081373; PMCID: PMC7602939.
Tsugawa, Hiroshi et al. “MS-DIAL: data-independent MS/MS deconvolution for comprehensive metabolome analysis.” Nature methods vol. 12,6 (2015): 523-6. doi:10.1038/nmeth.3393
Horai, H. et al (2010), MassBank: a public repository for sharing mass spectral data for life sciences. J. Mass Spectrom., 45: 703-714. https://doi.org/10.1002/jms.1777
Katherine T. Peter et al., Application of Nontarget High Resolution Mass Spectrometry Data to Quantitative Source Apportionment, Environmental Science & Technology 2019 53 (21), 12257-12268 DOI: 10.1021/acs.est.9b04481
Mass-suite requires major dependencies:
Pandas 1.0.3 or higher
Numpy 1.16.5 or higher
Scikit-learn 0.23.0 or higher
Scipy 1.4.1 or higher
pymzml 2.4.6 or higher
PeakUtils 1.3.3 or higher
plotly 4.5.2 or higher
Optional dependencies for machine-learning:
Keras 2.3.1
Tensorflow 2.0.0
Pytorch 1.4.0 or higher

## Slide 23: Thanks!