## Slide 1: Capstone Project Update
First phase 5/11

## Slide 2: Progress update
First phase: Finished!
Peak picking & assessment
Alignment & summary
Preliminary workflow integration
Second phase:
Clustering brainstorm & algorithm development
Establishment of the dilution prediction model
Multiple source tracking workflow development
Third phase:
Code testing, debugging and pack up for different versions towards user needs
Add more features

## Slide 3: Progress update

## Slide 4: Peak picking
  Mainly based on pymzml package, which provided a high efficiency access to the raw data even during iterations
  Single file/batch files option available
Mzml file import
  MS1/MS2 scan selection
  Noise removal
Raw data cleaning
  Mainly based on peakUtils package – similar to scipy.signal package
  Utilized DNN model developed from TF to assess the peaks
  In the export peak table, also added modeling score for user to define if to retain the features
Peak picking & peak table export

## Slide 5: Sample output

## Slide 7: Alignment
Functionality
  Reads in .csv files created from peak picking
  1 spreadsheet representative of all samples
Method
  Initial reference data frame created from first sample
  Other rows cross referenced for overlap
    Additional rows added to reference as needed
Calculates averages similarly to commercial output

## Slide 8: Alignment example output

## Slide 9: Main features
General:
  First package on python which provide full workflow from data import to alignment result
  Light memory usage make it possible to be run on personal laptops (~4min per sample at 5000 noise threshold under current tests)
  Hyak supercomputer utilization as remote data processing option
  More customization space for user while still have the default ‘one click’ script
  All workflow validated with MSdial sample outputs
Peak picking
  Boost up the large file processing time by pymzml port
  Provide assessment scores to improve the data quality by user needs
Alignment
  Can do the alignment for 100+ files in ~10 min
  Allows user to define mz, rt errors, and in what file type they want to save as

## Slide 10: Main features
Provided flexible options to users:
Integrated script
Mzml in, spreadsheet out
Python package
Function combinations
More tools:
Visualization
Ms2 library search

## Slide 11: User cases

## Slide 12: Next steps
Clustering algorithm development – second phase
  Literature reviews – why to do and how to do
  Algorithm development
    Feature grouping algorithm
    Prediction/source tracking model development
  Validation and application – start from data at one place to create the ‘box’
Package development -- third phase & future works
  Contribute the whole workflow as a user friendly and useful tools towards all MS users
  Leave out spaces for further development and customization according to needs
  Interactive GUI/webtools

## Slide 13: Q&A

## Slide 14: Brainstorm
Clustering:
  How to find clustering – Q1
    Based on data
    Based on visual
  How to use the clustering to achieve our goals – Q2
    Dilution prediction
    Source tracking